## Slide 1: Purpose
Introduce the basic concept of FTL (Flash Transition Layer) in SSD, since computer science does not cover SSD-related course
Book: 深入淺出 SSD

## Slide 2
die
plane
block
page
smallest unit that can independently execute commands
or report status
(die interleave)
…
…
…
…

## Slide 3
empty data
valid data
invalid data
Only consider 1 plane in this project
…
…
die
plane
block
page

## Slide 4
Only consider 1 plane in this project
…
…
empty data
valid data
invalid data
die
plane
block
page

## Slide 5
…
…
empty data
valid data
invalid data
die
plane
block
page

## Slide 6
…
…
empty data
valid data
invalid data
die
plane
block
page
Garbage Collection (GC)
Find a block that contains most invalid data
Move the valid data to an empty block
  No move operation in NAND Flash
  Must decompose to read, and then write

## Slide 7
…
…
empty data
valid data
invalid data
die
plane
block
page
Garbage Collection (GC)
Erase to get new empty block

## Slide 8: Scenario
The unit in user’s view
  sector (512 B)
The addressing scheme
  logical block address (lba)
The unit in NAND Flash’s view
  page (4KB)
The addressing scheme
  physical page address (ppa)
sector: 512 Bytes
page: 4096 Bytes
Reference: https://www.techtarget.com/whatis/definition/logical-block-addressing-LBA

## Slide 9: API Design
writeData (lba, sector_cnt, *source_data)
readData (lba, sector_cnt, *tar_data)
programPage (pca, *source_data)
readPage (pca, *tar_data)
eraseBlock(block)
FTL
(Flash Transition Layer)
1
2
3
unit conversion, table mapping
NAND Flash
User

## Slide 10: FTL
lba0
lba1
lba2
lba3
lba4
lba5
lba6
lba7
lpa 0
lba8
lba9
lba10
lba11
lba12
lba13
lba14
lba15
lpa 1
lba 8n
lba 8n+1
lba 8n+2
lba 8n+3
lba 8n+4
lba 8n+5
lba 8n+6
lba 8n+7
lpa n
…
ppa
lpa to which ppa is decided by FTL
FTL can calcutae lpa from lba
FTL decide write lpa to which ppa
So, we can construct a lpa to ppa mapping table (l2p table)

## Slide 11: Something you should think about
The number of valid/invalid data in a block
Which ppas are vaild/invalid
Which blocks are empty
When page data is moved because of erase, how to know the corresponding lpa and update lpa to ppa table?

## Slide 12: Conclusion
Erase before write
The units of erase, program and read are different
  erase: block
  program/read : page
  some read commands can read in plane unit, we exclude this case in the project
FTL task
  unit conversion
  table mapping
  ppa allocation

## Slide 13
die
plane
block
page
die
plane
block
page